## Slide 1: Wearable Computing Systems eyeDrops
Lab Course 2016 / 2017
Marlene Fiedler
Lorenz Miething
Benjamin Thiemann
Albert-Ludwigs-Universität Freiburg
Notes: Begrüßung
Name
Thema

## Slide 2: Contents
Eye blink detection – proof of concept
Components
Clip design
Printed circuit board
Blurry screen
Project plan

## Slide 3: Eye blink detection – Sensors
Ambient light sensor
  APDS 9600 RGB ambient light and gesture sensor
    First success but slow and not robust (active)
https://cdn.sparkfun.com//assets/parts/9/6/0/3/12787-02.jpg

## Slide 4: Eye blink detection – Sensors
Ambient light sensor
  APDS 9600 RGB ambient light and gesture sensor
  Self built alternative using photodiode and analogue signal
    Very fast but not robust (passive)

## Slide 5: Eye blink detection – Sensors
Ambient light sensor
  APDS 9600 RGB ambient light and gesture sensor
  Self built alternative using photodiode and analogue signal
Proximity sensor
  VCNL 4010 ambient light and proximity sensor (active)
    Fast enough and robust
https://cdn-shop.adafruit.com/1200x900/466-05.jpg

## Slide 6: Eye blink detection – Software
Capture record and visualize data using Processing

## Slide 7: Eye blink detection – Software
Capture and visualize data using Processing
Analyse and develop algorithm using MATLAB

## Slide 8: Components
RFDuino
  Arduino compatible microcontroller
  Bluetooth low energy RF module
http://www.rfduino.com/wp-content/uploads/2014/03/RFD22301.Prospective.Top_.png
Notes: Arduino compatible Microcontroller
With a bluetooth low energy RF module
We use SMD version
ADC
Interfaces: I²C, UART, SPI, GPIO
Wireless communication with iOS and android smartphones

## Slide 9: Components
RFDuino
  Arduino compatible microcontroller
  Bluetooth low energy RF module
VCNL4020
  Ambient light sensor
  Proximity sensor
  Interrupt function
http://www.vishay.com/docs/83476/vcnl4020.pdf
Notes: I²C
Ambient light not used right now, maybe later

## Slide 10: Components
RFDuino
  Arduino compatible microcontroller
  Bluetooth low energy RF module
VCNL4020
  Ambient light sensor
  Proximity sensor
  Interrupt function
BNO055
  Absolute orientation sensor
http://www.mouser.com/images/microsites/Bosch_BNO055.jpg
Notes: optional
Gyroscope, accelerometer, geomagnetic sensor
I²C, UART

## Slide 11: Assembly on glasses
Notes: Gyroscope, accelerometer, geomagnetic sensor
I²C, UART

## Slide 12: Assembly on glasses
Notes: Gyroscope, accelerometer, geomagnetic sensor
I²C, UART

## Slide 13: Assembly on glasses
Notes: Gyroscope, accelerometer, geomagnetic sensor
I²C, UART

## Slide 14: Clip
Notes: Gyroscope, accelerometer, geomagnetic sensor
I²C, UART

## Slide 15: Clip
www.anz-verlag.de
Notes: Gyroscope, accelerometer, geomagnetic sensor
I²C, UART

## Slide 16: PCB for VCNL4020

## Slide 17: PCB for VCNL4020

## Slide 18: PCB for VCNL4020 – smaller

## Slide 19: PCB for VCNL4020 – smaller

## Slide 20: PCB for VCNL4020

## Slide 21: PCB for RFDuino

## Slide 22: Blurry screen
First trial: platform independent (Java, Python)
Second trial: only Mac OS X (Objective-C)
Uses CoreGraphics framework
Menubar application
Platform independent application will control the blurring
Version for Linux and/or Windows if we have time

## Slide 23: Blurry screen
DEMO

## Slide 24: Project plan

## Slide 25: Eye blink detection
DEMO

## Slide 26
Thank you for your attention!

## Slide 27: Ball Joint
Notes: Gyroscope, accelerometer, geomagnetic sensor
I²C, UART